---------------------------------------------------------------------------

SECTION 1 - CHEMICAL PRODUCT AND COMPANY IDENTIFICATION

---------------------------------------------------------------------------

CHEMICAL PRODUCT IDENTIFICATION:

PRODUCT ID  . . . . . . . . . . : 4442SP.100.x.

PRODUCT CLASS . . . . . . . . . : PAINT, SOLVENT BASE

TRADE NAME  . . . . . . . . . . : WHITE VINYL BASECOAT

FORMULA ID  . . . . . . . . . . : 4442SP.100.x

MSDS PREPARATION DATE . . . . . : 3/05/2010

MANUFACTURER IDENTIFICATION:

NAME  . . . . . . . . . . . . : NANOCHEM TECHNOLOGIES

ADDRESS . . . . . . . . . . . : 1203 KENT STREET

ELKHART, IN 46514

TELEPHONE . . . . . . . . . . : 574-970-2436

EMERGENCY CONTACT . . . . . . : CHEMTREC

EMERGENCY TELEPHONE . . . . .: (800) 424-9300

---------------------------------------------------------------------------

SECTION 2 - COMPOSITION/INFORMATION ON HAZARDOUS INGREDIENTS

---------------------------------------------------------------------------

1. CAS#  67-64-1

ACETONE

PCT BY WT:    2-7%    VAPOR PRESSURE:    185 MMHG @ 68F

EXPOSURE LIMIT:

ACGIH TLV/TWA:        500 ppm TWA

ACGIH TLV/STEL:       750 ppm TWA

OSHA PEL/TWA:         1000 ppm TWA

LC50:                 Inhalation (Rat) – 5.8g /kg

LD50:                 Oral (Rat) – 1.0 g/kg

CA PROPOSITION 65:    No

---------------------------------------------------------------------------

2. CAS#  123-86-4

BUTYL ACETATE

PCT BY WT:    1-5%    VAPOR PRESSURE:    8.7 MMHG @ 68F

EXPOSURE LIMIT:

ACGIH TLV/TWA:        150 ppm TWA

ACGIH TLV/STEL:       200 ppm STEL

OSHA PEL/TWA:         150 ppm TWA

LC50:                 Inhalation (Rat) – 1800 ppm

LD50:                 Oral (Rat) – 14.1 g/kg

CA PROPOSITION 65:    Yes

--------------------------------------------------------------------------

3. CAS#  108-88-3

TOLUENE

PCT BY WT:    4-8%    VAPOR PRESSURE:    26 MMHG @ 68F

EXPOSURE LIMIT:

ACGIH TLV/TWA:        50 ppm TWA

ACGIH TLV/STEL:

OSHA PEL/TWA:         50 ppm TWA

LC50:                 No Data

LD50:                 No Data

CA PROPOSITION 65:    Yes

---------------------------------------------------------------------------

4. CAS#  108-65-6

PM ACETATE

PCT BY WT:       7-15%     VAPOR PRESSURE:    3.7 MMHG@ 68F

EXPOSURE LIMIT:

ACGIH TLV/TWA:             100 ppm TWA

OSHA PEL/TWA:              100 ppm TWA

LC50:                      Inhalation   (Rat)  4000 PPM/6H

LD50:                      Oral (Rat) – 8.5 g/kg

CA PROPOSITION 65:         Yes

---------------------------------------------------------------------------

5. CAS#  78-93-37

METHYL ETHYL KETONE

PCT BY WT:    5-10%   VAPOR PRESSURE:    78.0 MMHG @ 68F

EXPOSURE LIMIT:

ACGIH TLV/TWA:        200  ppm TWA

ACGIH TLV/STEL:       300  ppm STEL

OSHA PEL/TWA:         200 ppm TWA

LC50:                 Inhalation (Rat) – 23,500 mg/m3/8H

LD50:                 Oral (Rat) – 2737 mg/kg

CA PROPOSITION 65:    Yes

---------------------------------------------------------------------------

6.  CAS#  11012-3

METHYL ISOAMYL KETONE

PCT BY WT:    2-5%    VAPOR PRESSURE:    3.7 MMHG @ 68F

EXPOSURE LIMIT:

ACGIH TLV/TWA:        50 ppm TWA

ACGIH TLV/STEL:          ppm STEL

OSHA PEL/TWA:         150ppm TWA

Lc50:                 Inhalation   (Rat)  5000 ppm

LD50:                 Oral (Rat) – 2.0 g/kg

CA PROPOSITION 65:    Yes

----------------------------------------------------------------------------

7.   CAS#  111-76-2

2-BUTOXY-ETHANOL

PCT BY WT:    2-4%    VAPOR PRESSUE:     0..98MMHG @ 68°F

EXPOSURE LIMIT

ACGIH TLV/TWA:        20 ppm TWA

OSHA PEL/TWA:         50 ppm TWA

LC50:                 Inhalation (Rat) – 700 ppm/4H

LD50:                 Oral (Rat) – 3.0 g/kg

CA PROPOSITION 65:    No

---------------------------------------------------------------------------

8.   CAS# 110-19-0

ISOBUTYL ACETATE

PCT BY WT:    5-10    VAPOR PRESSURE:     76.0 MMHG@68 °F

EXPOSURE LIMIT:

ACGIH TLV/TWA:	     100 ppm TWA

ACGIH TLV/STEL:	     150 ppm TWA

LC50:		     Inhalation  (Rat)  100ppm

LC50:		     Oral   (Rat)      5600 mg/kg

CA PROPOSITION 65:    Yes

----------------------------------------------------------------------------

------------------------------------------------------------------------------

***************************************************************************

This product contains one or more reported carcinogens or suspected

carcinogens which are noted in Section 3, Hazards Identification,

CARCINOGENICITY.

***************************************************************************

***************************************************************************

MSDS 4442SP.100.x

This product contains one or more Hazardous Air Pollutants.

***************************************************************************

***************************************************************************

This product contains pigments, which may become a dust nuisance when

removed by abrasive blasting, sanding, or grinding.

***************************************************************************

***************************************************************************

This product contains one or more reported or suspected reproductive

toxins.

***************************************************************************

***************************************************************************

---------------------------------------------------------------------------

SECTION 3 - HAZARDS IDENTIFICATION

---------------------------------------------------------------------------

POTENTIAL HEALTH EFFECTS

EYES:  Exposure to liquid may cause mild eye irritation.  Symptoms

may include stinging, tearing, and redness.

SKIN:  May cause skin defatting with prolonged exposure.  Exposure may

cause skin irritation.  Prolonged or repeated exposure may dry

the skin.

INHALATION:  Causes mild respiratory irritation.  Breathing large

amounts may be harmful.  Symptoms of exposure may

include irritation (nose, throat, respiratory tract)

and CNS depression.

INGESTION:  Swallowing small amounts of this product during normal

handling is not likely to cause harmful effects, but

swallowing large amounts may be harmful.

CHRONIC EFFECTS

NOTICE:  Reports have associated repeated and prolonged occupational

exposure to solvents with permanent brain and nervous system damage.

Intentional misuse by deliberately concentrating and inhaling the contents

may be harmful or fatal.  May cause respiratory and/or skin sensitization.

MEDICAL CONDITIONS AGGRAVATED BY EXPOSURE

Any pre-existing respiratory or eye/skin conditions.

POSSIBLE ROUTES OF ENTRY

Inhalation, ingestion, skin absorption.

---------------------------------------------------------------------------

SECTION 4 - FIRST AID MEASURES

---------------------------------------------------------------------------

EMERGENCY FIRST AID:

EYE CONTACT

If irritation or redness develops, move victim away from exposure and into

fresh air.  Flush eyes with clean water, holding eyelids apart.  If

symptoms persist, seek medical attention.

SKIN CONTACT

Remove contaminated shoes and clothing, and flush affected area with large

amounts of water.  If skin surface is damaged, apply a clean dressing and

seek medical attention.  If skin surface is not damaged, cleanse affected

area thoroughly by washing with mild soap and water.  If irritation or

redness develops, seek medical attention.  Launder clothing before reuse.

INHALATION

If respiratory symptoms develop, move victim away from source of exposure

and into fresh air.  If symptoms persist, seek medical attention.  If

MSDS 4442SP.100.x

victim is not breathing, immediately begin artificial respiration.  If

breathing difficulties develop, oxygen should be administered by qualified

personnel.  Seek immediate medical attention.  Keep person warm & quiet.

INGESTION

Aspiration hazard.  Do not induce vomiting or give anything by mouth

because this material can enter the lungs and cause severe lung damage.

If the victim is drowsy or unconscious, place on left side with head down.

If possible, do not leave victim unattended.  Seek immediate medical

attention.

NOTE TO PHYSICIAN:

Not Applicable.

---------------------------------------------------------------------------

SECTION 5 - FIRE FIGHTING MEASURES

---------------------------------------------------------------------------

FIRE AND EXPLOSIVE PROPERTIES OF THE CHEMICAL:

Flammability Classification . . . . . : FLAMMABLE Liquid-Class III

Flashpoint  . . . . . . . . . . . . . : -20C

Explosive limits . . . . . . . . . : Lower    -    2.6%

Upper    -   12.8%

EXTINGUISHING MEDIA

Use National Fire Protection Association (NFPA) Class B extinguisher

(carbon dioxide, dry chemical or foam).

FIRE-FIGHTING INSTRUCTIONS

During fire, a water spray can scatter flames and should be used

by experienced firefighters.  Firefighters should wear self-contained

breathing apparatus with a full face piece operated in the positive

pressure mode when fighting fires.  Isolate damage area, keep

unauthorized personnel out.  Avoid spreading burning liquid with water

used for cooling purposes.

UNUSUAL FIRE AND EXPLOSION HAZARDS

Flammable liquid.  Forms  flammable mixtures with air at or above

the flash point.  This product can accumulate static charges, which can

cause fire or explosion.  This liquid is volatile and gives off invisible

vapors.  Either the liquid or vapor may settle in low areas or travel

some distance along the ground or surface to ignition sources where

they may ignite or explode and flash back.

---------------------------------------------------------------------------

SECTION 6 - ACCIDENTAL RELEASE MEASURES

---------------------------------------------------------------------------

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED

Eliminate all ignition sources.  Spilled material may be absorbed into

an appropriate absorbent material.  Prevent spilled material from entering

sewers, storm drains, other authorized treatment drainage systems, and

natural waterways.  Stop spill/release if it can be done, and stay away

from spill.  Isolate danger and keep unauthorized personnel out.

Use non-sparking tools and explosion-proof equipment.

CLEAN-UP

Warn occupants in surrounding and downwind areas of fire and explosion

and to stay clear.  Remove from surface with suitable absorbents.  If

allowed by local authorities, sinking and/or suitable dispersants may be

used in non-confined waters.

---------------------------------------------------------------------------

SECTION 7 - HANDLING AND STORAGE

---------------------------------------------------------------------------

MSDS 4442SP.100.x

HANDLING

Keep container closed.  Handle and open container with care.  Open

container slowly to relieve any pressure.  Do NOT cut, weld or puncture

on or near container.

STORAGE   Keep container(s) tightly closed.  Use and store this product in a

cool, dry, well-ventilated area away from heat, direct sunlight, hot metal

surfaces, and all sources of ignition.  Keep away from any incompatible

material.  Protect container(s) against physical damage.

SPECIAL COMMENTS

WARNING:  Sudden release of hot organic chemical vapors or mists from

process equipment operating at elevated temperatures and pressures, or

sudden ingress of air into vacuum equipment, may result in ignitions

without the presence of obvious ignition sources.

---------------------------------------------------------------------------

SECTION 8 - EXPOSURE CONTROLS, PERSONAL PROTECTION

---------------------------------------------------------------------------

VENTILATION

Provide sufficient mechanical (general and/or local exhaust)

ventilation to maintain exposure below TLV(s).

RESPIRATORY PROTECTION

If personal exposure cannot be controlled below applicable limits by

ventilation, wear a properly fitted organic vapor/particulate respirator

approved by NIOSH for protection against chemicals in Sections (2 &/or 15).

EYE PROTECTION

Wear safety glasses or goggles to protect against exposure.  Chemical

splash goggles in compliance with OSHA regulations are advised; however,

OSHA regulations also permit other types of safety glasses.

PROTECTIVE GLOVES

Appropriate disposable gloves are acceptable, such as, Nitrile rubber

gloves.

---------------------------------------------------------------------------

SECTION 9 - PHYSICAL AND CHEMICAL PROPERTIES

---------------------------------------------------------------------------

Physical State . . . . . . . . . . . .:   LIQUID

Vapor Pressure . . . . . . . . . . .  :

Vapor Density . . . . . . . . . . . . :   HEAVIER THAN AIR

Boiling Point Range . . . . . . . . . :   Lower  -  133.0   øF

Higher -  408.0   øF

Specific Gravity  . . . . . . . . . . :   1.202

Weight per Volume . . . . . . . . . .  :  10.0 LB/GL

VOC - Total (lbs./gal). . . . . . . . :   5.59 LBS./GAL., 5.53 LBS/GAL.

MINUS EXEMP SOLVENT

Evaporation Rate . . . . . . . . . . .:   3.7 (n-Butyl Acetate = 1)

Volatile by Weight  . . . . . . . . . :   55.0%

Volatile by Volume  . . . . . . . . . :   73.2%

---------------------------------------------------------------------------

SECTION 10 - STABILITY AND REACTIVITY

---------------------------------------------------------------------------

STABILITY

This product is stable.

INCOMPATIBILITIES (Materials to Avoid)

This product can react violently with strong oxidizing agents such

as chlorine, oxygen, or strong oxidizing acids, such as, nitric and

MSDS 4442SP.100.x

sulfuric.

HAZARDOUS POLYMERIZATION

Will not occur.

CONDITIONS TO AVOID

Avoid heat, sparks, open flames and other sources of ignition.

HAZARDOUS PRODUCTS OF DECOMPOSITION

Heating to decomposition, as in a fire or welding, may produce

hazardous fumes.  Fumes may contain carbon monoxide, carbon dioxide and oxides of nitrogen.

---------------------------------------------------------------------------

SECTION 11 - TOXICOLOGICAL INFORMATION

---------------------------------------------------------------------------

No data at this time.

---------------------------------------------------------------------------

SECTION 12 - ECOLOGICAL INFORMATION

---------------------------------------------------------------------------

No data at this time.

---------------------------------------------------------------------------

SECTION 13 - DISPOSAL CONSIDERATIONS

---------------------------------------------------------------------------

WASTE DISPOSAL

Dispose of this product in accordance with applicable local,

county, state and federal regulations, by incinerating, or treating and

disposing in approved facility.  Do not incinerate closed containers.

---------------------------------------------------------------------------

SECTION 14 - TRANSPORT INFORMATION

---------------------------------------------------------------------------

DOT HAZARD CLASS . . . . . . . . .: 3

DOT PACKAGING GROUP . . . . . . . : PG II

DOT LABEL . . . . . . . . . . . . : RED

DOT SHIPPING NAME . . . . . . . . : PAINT

DOT PLACARD . . . . . . . . . . . : FLAMMABLE

UN/NA NUMBER . . . . . . . . . . .: UN1263

-----------------------------------------------------------------------------

SECTION 15 - REGULATORY INFORMATION

---------------------------------------------------------------------------

U.S. FEDERAL REGULATORY INFORMATION

TSCA SECTION 8(b) - INVENTORY STATUS:

All components of this product are either listed on the U.S. Toxic

Substances Control Act (TSCA) inventory of chemicals or are otherwise

compliant with TSCA Regulations.

SECTION 16 - OTHER INFORMATION

---------------------------------------------------------------------------

Prepared by . . . . . . . . . . . . . :

Date of issue . . . . . . . . . . . . : 3/05/2010

Last Revision Date  . . . . . . . . . : 3/05/2010

MSDS Prepared for . . . . . . . . . . : 4442SP.100.x

MSDS Last Prepared  . . . . . . . . . : NONE

HMIS Rating:        Health-  3       Flammability-  3

Reactivity-  0

***************************************************************************

This Material Safety Data Sheet conforms to the Hazard Communication

Standard, 29 CFR 1910.1200(g)(4).

MSDS 4442SP.100.x

The above information pertains to this product as currently formulated

and is based on the information available, as of this date.  Addition of

reducers or other additives to this product may substantially alter the

composition and hazards of the product.  Since conditions of use are out-

side our control, we make no warranties, express or implied, and assume

no liability in connection with any use of this information.

---------------------------------------------------------------------------

***************************************************************************

Abbreviations used: int.- interior; ext.- exterior; MSDS - Material Safety

Data Sheet; HMIS - Hazardous Materials Information System; CAS - Chemical

Abstracts Services; pct - percent; wt - weight; mm Hg - millimeters of

mercury; F - Fahrenheit; ACGIH - American Conference of Governmental

Industrial Hygienists; TLV - Threshold Limit Value; OSHA - Occupational

Safety and Health Administration; PEL - Permissible Exposure Limit; TWA -

Time-Weighted Average; STEL- Short Term Exposure Limit; N/A- Not applicable

IARC - International Agency for Research on Cancer; NE - Not established

NTP - National Toxicological Program; CFR - Code of Federal Regulations;

OSHA - Z 29CFR 1910, Subpart Z; VOC - Volatile Organic Compounds; TCC -

Tag Closed Cup; LEL - Lower Explosive Limit; Mg/m3 or Mg/Cu M - milligram

per cubic meter; mppcf - millions of particles per cubic foot; ppm - parts

per million; NIOSH - National Institute of Occupational Safety and Health;

MSHA - Mine Safety and Health Administration; CNS - Central Nervous System.